## Slide 1: Iron Man Suit Module Guide (1 to 7)
Power System, Flight, Exoskeleton, AI + HUD, Repulsor, Control, Armor

## Slide 2: 1. Power System
Component: Li-ion 24V Battery Pack + BMS
Includes OLED Display + LM35 Temp Sensor
Voltage Regulated to 5V/12V using Buck Converter
Arduino Monitors Voltage and Temperature
Code Snippet: analogRead(tempPin) * 0.488 → Celsius Voltage divider for battery monitoring OLED display via I2C

## Slide 3: 2. Flight System
Components: EDF Units, ESCs, Arduino, 24V Battery
Signal control via PWM (D9)
Test mounted on stable surface, not worn
Optional: MPU6050 Gyro for balance
Code Snippet: edf.attach(9) edf.writeMicroseconds(1500)

## Slide 4: 3. Exoskeleton
Material: Aluminum/Carbon Frame
Servo Motor Control via Flex Sensor
Arduino Nano + Servo (D9)
Voltage Divider for Flex Input
Code Snippet: int val = analogRead(flex); val = map(val, 600, 900, 0, 180); arm.write(val);

## Slide 5: 4. AI + HUD
Raspberry Pi + USB Mic + OLED Display
Python SpeechRecognition + pyttsx3
Voice-activated system feedback
HUD using transparent OLED or glasses
Code Snippet: audio = r.listen(source) command = r.recognize_google(audio) engine.say(command)

## Slide 6: 5. Repulsor
10W LED + Boost Converter
Hand Gesture Trigger (Flex/Accel)
Sound Module (DFPlayer) + Arduino
Mounted in Palm with LED Flash + Sound
Code Snippet: analogWrite(LED, 255); // Blast DFPlayer -> Audio Trigger

## Slide 7: 6. Control System
5x Flex Sensors (fingers) + MPU6050
Wireless TX/RX (e.g. NRF24L01)
Arduino Reads Gestures and Sends to Suit
Mapped to Motor or LED Actions
Code Snippet: int ax = mpu.getAccelerationX(); Serial.println(ax);

## Slide 8: 7. Armor
Material: Polycarbonate / 3D-Printed ABS
Painted with Automotive Red + Gold
Arc Reactor: LED Ring + Diffuser
Fades using analogWrite on PWM pin
Code Snippet: for (int i = 0; i < 255; i++) { analogWrite(LED, i); delay(10); }